; ****************************************************************
; Electronic Wallet using the PN532 RFID Module
; Uses 13.56-MHz MIFARE Classic 1k tags/cards
;
; Assumes that we are using the default 8-MHz internal clock.
;
; All routines will exit pointing to bank0.
; ****************************************************************
;
        LIST P=PIC16F688
        #INCLUDE <p16f688.inc>

        ERRORLEVEL	0,	-302	;suppress bank selection messages

        __CONFIG _FOSC_INTOSCIO & _WDT_OFF & _PWRTE_ON & _MCLRE_OFF & _BOD_OFF & _CPD_OFF & _CP_OFF

; LCD interface defines
LCD_Data4 EQU 0 ;RC0: LCD data line 4
LCD_Data5 EQU 1 ;RC1: LCD data line 5
LCD_Data6 EQU 2 ;RC2: LCD data line 6
LCD_Data7 EQU 3 ;RC3: LCD data line 7
#define LCD_TRIS TRISC
#define LCD_PORT PORTC
#define Max_Line 8 ;Max hex chars per line (1 hex = 2 ASCII)

#define Trail_Blk 7 ;ID of Trailer Block (holds keys)
#define Data_Blk 6 ;ID of Data Block (holds credits)
#define Bkup_Blk 5 ;ID of Backup Data Block (holds credits)
#define Resp_TFI 0xD5 ;TFI for response messages from reader

#define Def_Key1 0xFF ;first byte of default key
#define Def_Key2 0xFF
#define Def_Key3 0xFF
#define Def_Key4 0xFF
#define Def_Key5 0xFF
#define Def_Key6 0xFF ;last byte of default key

#define My_Key1 0x01 ;first byte of new key
#define My_Key2 0x02
#define My_Key3 0x00
#define My_Key4 0x01
#define My_Key5 0x04
#define My_Key6 0x08 ;last byte of new key

;Set for increment amount (packed BCD)
#define Inc1 0x00 ;1/10
#define Inc100 0x00 ;100/1000
#define Inc10_000 0x00 ;10/100 thousand
#define Inc_Mill 0x02 ;1/10 million

;Set for decrement amount (packed BCD)
#define Dec1 0x00 ;1/10
#define Dec100 0x00 ;100/1000
#define Dec10_000 0x50 ;10/100 thousand
#define Dec_Mill 0x00 ;1/10 million

;PORTA Defines
#define Enable_T TRISA, 0 ;LCD enable
#define Enable PORTA, 0 ;LCD enable
#define Select_T TRISA, 1 ;LCD cmd/data mode select
#define Select PORTA, 1 ;LCD cmd/data mode select
#define Init_Sw PORTA, 4;2 ;0=zero the credits and change the keys
#define Inc_Sw PORTA, 3 ;0=increment, 1=decrement

Cmnd_Mode EQU 00 ;LCD register select command mode
Data_Mode EQU 01 ;LCD register select data mode

;Defines
RX_Port EQU 05 ;PORTC5 - Serial receive
TX_Port EQU 04 ;PORTC4 - Serial transmit (unused)

Bank0_Data UDATA 0x20 ;Bank 0 data
Delay_Cnt RES 1 ;Delay Counter
LCD_Data RES 1 ;Temporary holder for LCD data
Reg_Select RES 1 ;LCD register select flag
BCD_Byte RES 1 ;used for conversion to ASCII
Dummy RES 1 ;dummy variable
Temp_ASC RES 1 ;Temporary variable used in Make_ASCII
Byte_Count RES 1 ;byte counter
RX_Byte RES 1 ;serial receive byte
New_Msg RES 1 ;new message received flag
Save_W RES 1 ;save the W register during interrupts
Save_Status RES 1 ;save the Status register during interrupts
Checksum RES 1 ;checksum for commands
UID1 RES 1 ;user ID of card/tag
UID2 RES 1 ;user ID of card/tag
UID3 RES 1 ;user ID of card/tag
UID4 RES 1 ;user ID of card/tag
Tag_Blk_Num RES 1 ;Tag Block Number
Read_Cnt RES 1 ;counter for reading receive buffer
Targ_Ptr RES 1 ;pointer to target value for buffer read
TFI_Found RES 1 ;TFI was found in the response message
Millions RES 1 ;Packed BCD (millions and 10 millions)
Ten_Thou RES 1 ;Packed BCD (10 thousands and 100 thousands)
Hundreds RES 1 ;Packed BCD (hundreds and thousands)
Ones RES 1 ;Packed BCD (ones and tens)
Carry RES 1 ;carry flag from DAA routine
Borrow RES 1 ;borrow flag from DAS routine
Comp_1 RES 1 ;1's complement credit amount LS byte
Comp_2 RES 1
Comp_3 RES 1
Comp_4 RES 1 ;1's complement credit amount MS byte
Cmd_Echo RES 1 ;byte after TFI in response
Cmd_Stat RES 1 ;command status in response
Try_Def RES 1 ;if scan fails then try default key
Disp_All RES 1 ;1: display entire receive buffer
        ;0: display just data bytes
Line_Brk RES 1 ;LCD line break after this value
Reinit_Tag RES 1 ;tag data corrupt so try reinit

Tag_Message UDATA 0x50 ;ACK, Preamble, Message Response
Byte1 RES 1 ;First byte
Byte2 RES 1
Byte3 RES 1
Byte4 RES 1
More_Bytes RES d'25' ;The rest of the message

;-----------------------------------
; Macros
;-----------------------------------

;Decimal adjust passed argument after BCD addition
DAA macro var1
        MOVFW var1
        ADDLW -0x0A
        BTFSC STATUS, DC ;LSD > 9?
        ADDLW 0x06 ;yes so fix it
        ADDLW 0x0A ;add back in what we took out
        CLRF Carry
        ADDLW -0xA0
        BTFSC STATUS, C ;MSD > 9?
        BSF Carry, 0 ;yes
        ADDLW 0xA0 ;add back in what we took out
        BTFSC Carry, 0
        ADDLW 0x60
        MOVWF var1 ;copy result to passed in variable
        endm

;Decimal adjust passed argument after BCD subtraction
DAS macro var1
        MOVFW var1
        ADDLW 0x06
        BTFSC STATUS, DC ;LSD > 9?
        ADDLW -0x06 ;yes so fix it
        ADDLW -0x06 ;subtract back out what we put in
        CLRF Borrow
        ADDLW 0x60
        BTFSC STATUS, C ;MSD > 9?
        BSF Borrow, 0 ;yes
        ADDLW -0x60 ;subtract back out what we put in
        BTFSC Borrow, 0
        ADDLW -0x60
        MOVWF var1 ;copy result to passed in variable
        endm

;-----------------------------------
; Program code starts here
;-----------------------------------

RESET CODE 0x00
        GOTO Init

;Interrupt Handler
Int_Vec CODE 0x04
        BCF PIE1, RCIE ;serial RX interrupt enable
        MOVWF Save_W
        SWAPF STATUS, W
        MOVWF Save_Status
Chk_Ovr BTFSS RCSTA, OERR ;receive buffer overflow error:
        GOTO RX_Int1 ;no
        CALL Overflow
        GOTO Ret_Prep

RX_Int1 MOVFW RCREG ;read RX buffer (clears interrupt)
        MOVWF RX_Byte
        BTFSC New_Msg, 0 ;first character of new message?
        GOTO RX_Int2 ;no
        CLRF Byte_Count

RX_Int2 BSF New_Msg, 0
        MOVLW LOW Byte1
        ADDWF Byte_Count, W
        MOVWF FSR
        MOVFW RX_Byte
        MOVWF INDF ;save to buffer as indexed by Byte_Count
        INCF Byte_Count, F

RX_Int3 MOVFW RX_Byte
        BTFSC PIR1, RCIF ;another RX interrupt?
        GOTO Chk_Ovr ;yes

Ret_Prep SWAPF Save_Status, W
        MOVWF STATUS
        SWAPF Save_W, F
        SWAPF Save_W, W
        BSF PIE1, RCIE ;serial RX interrupt enable
        RETFIE

;Main code
Init NOP ;error if go directly to BANKSEL
        BANKSEL TRISA ;bank1
        BCF Enable_T ;output
        BCF Select_T ;output
        BCF LCD_TRIS, LCD_Data4
        BCF LCD_TRIS, LCD_Data5
        BCF LCD_TRIS, LCD_Data6
        BCF LCD_TRIS, LCD_Data7
        CLRF ANSEL ;set all as digital
        MOVLW 0x70
        MOVWF OSCCON ;set for 8-MHz internal clock
        BCF OPTION_REG, NOT_RAPU ;enable weak pull-ups
        BSF PIE1, RCIE ;serial RX interrupt enable

        BANKSEL PORTA ;bank0
        MOVLW 0x07
        MOVWF CMCON0 ;turn off comparators
        CLRF Byte_Count
        CLRF New_Msg
        CLRF Disp_All
        CALL Init_Serial

        BTFSS STATUS, NOT_TO ;reset due to WDT?
        GOTO Scan_Loop ;yes
        CLRF Try_Def
        CLRF Reinit_Tag
        CALL Delay100ms ;wait for LCD to get ready
        CALL Init_LCD

Module_Init CALL Send_Init
        BTFSS New_Msg, 0 ;response from reader?
        GOTO Module_Init ;no

Scan_Loop MOVLW Data_Blk
        MOVWF Tag_Blk_Num

        ;Find a tag
        CALL Scan_Tag
        CALL Disp_UID ;comment out if not needed

        ;Found a Tag so authorize for reads/writes
        CALL Auth_Tag
        CALL Auth_Msg ;comment out if not needed

        ;Manual init switch
        BTFSS Init_Sw ;initialize tag?
        CALL Init_Tag ;yes

        ;Initialize a new tag (change keys and set credits to zero)
        ;This is done if the tag cannot be authorized using My_Key
        BTFSC Try_Def, 0
        CALL Init_Tag

        ;Attempt to initialize a tag if both sets of data are corrupted
        BTFSC Reinit_Tag, 0
        CALL Init_Tag

        ;Read data
        CALL Read_Tag
        CALL Get_Credit
        SUBLW d'1'
        BTFSS STATUS, Z ;valid data?
        GOTO Match_Fail ;no
        CALL Disp_Credit

        BTFSS Inc_Sw ;add credits?
        CALL Inc_Credit ;yes
        BTFSC Inc_Sw ;subtract credits?
        CALL Dec_Credit ;yes

        CALL Done_Msg

        GOTO Scan_Loop

;-----------------------------------
; RFID Messages
;-----------------------------------

;Initialize and wakeup RFID module
Send_Init MOVLW 0x55
        CALL TX_Serial
        MOVLW 0x55
        CALL TX_Serial
        MOVLW 0x00
        CALL TX_Serial
        MOVLW 0x00
        CALL TX_Serial
        MOVLW 0x00
        CALL TX_Serial
        MOVLW 0x00
        CALL TX_Serial ;add more zeros if needed to wake up

        ;Need to send SAM Config to get out of Low Vbat state
        CALL Preamble
        MOVLW 0x03
        CALL TX_Serial
        MOVLW 0xFD
        CALL TX_Serial
        MOVLW 0xD4
        CALL TX_Serial
        MOVLW 0x14 ;SAMConfiguration
        CALL TX_Serial
        MOVLW 0x01
        CALL TX_Serial
        MOVLW 0x17
        CALL TX_Serial
        GOTO Postamble

Send_ACK MOVLW 0x00
        CALL TX_Serial
        MOVLW 0x00
        CALL TX_Serial
        MOVLW 0xFF
        CALL TX_Serial
        MOVLW 0x00
        CALL TX_Serial
        MOVLW 0xFF
        CALL TX_Serial
        MOVLW 0x00
        CALL TX_Serial
        RETURN

;Get RFID module firmware version number (contained in
;the last three data words of the response message)
;Example: 01 06 07 is version 1.6.7
Firmware CALL Preamble
        MOVLW 0x02
        CALL TX_Serial
        MOVLW 0xFE
        CALL TX_Serial
        MOVLW 0xD4
        CALL TX_Serial
        MOVLW 0x02 ;GetFirmwareVersion
        CALL TX_Serial
        MOVLW 0x2A
        CALL TX_Serial
        GOTO Postamble

;Look for a tag
Scan_Tag CALL Preamble
        MOVLW 0x04
        CALL TX_Serial
        MOVLW 0xFC
        CALL TX_Serial
        MOVLW 0xD4
        CALL TX_Serial
        MOVLW 0x4A ;InListPassiveTarget
        CALL TX_Serial
        MOVLW 0x01 ;read one card (max=2)
        CALL TX_Serial
        MOVLW 0x00 ;106-kbps type A
        CALL TX_Serial
        MOVLW 0xE1
        CALL TX_Serial
        CALL Postamble
        CALL Scan_Msg
        CALL Find_Resp
        BTFSS TFI_Found, 0
        GOTO Scan_Tag
        CALL Get_UID
        RETURN

;Last four data words in the scan response are UID
;for Mifare Classic 1k tags
Get_UID MOVLW d'8' ;offset from TFI to UID
        ADDWF Targ_Ptr, F
        MOVLW LOW Byte1
        ADDWF Targ_Ptr, W ;index to RFCID
        MOVWF FSR
        MOVFW INDF
        MOVWF UID1
        INCF FSR, F
        MOVFW INDF
        MOVWF UID2
        INCF FSR, F
        MOVFW INDF
        MOVWF UID3
        INCF FSR, F
        MOVFW INDF
        MOVWF UID4
        RETURN

;Authunticate tag data sector using the defined Trailer block ID
Auth_Tag CALL Preamble
        MOVLW 0x0F
        CALL TX_Serial
        MOVLW 0xF1
        CALL TX_Serial
        MOVLW 0xD4
        MOVWF Checksum
        CALL TX_Serial
        MOVLW 0x40 ;InDataExchange
        ADDWF Checksum, F
        CALL TX_Serial
        MOVLW 0x01 ;number of targets
        ADDWF Checksum, F
        CALL TX_Serial
        MOVLW 0x60 ;authenticate with Key A
        ADDWF Checksum, F
        CALL TX_Serial
        MOVLW Trail_Blk ;Trailer block for data sector
        ADDWF Checksum, F
        CALL TX_Serial
        MOVLW My_Key1 ;Key A (6 bytes)
        BTFSC Try_Def, 0 ;failed previous scan?
        MOVLW Def_Key1 ;yes
        ADDWF Checksum, F
        CALL TX_Serial
        MOVLW My_Key2
        BTFSC Try_Def, 0 ;failed previous scan?
        MOVLW Def_Key2 ;yes
        ADDWF Checksum, F
        CALL TX_Serial
        MOVLW My_Key3
        BTFSC Try_Def, 0 ;failed previous scan?
        MOVLW Def_Key3 ;yes
        ADDWF Checksum, F
        CALL TX_Serial
        MOVLW My_Key4
        BTFSC Try_Def, 0 ;failed previous scan?
        MOVLW Def_Key4 ;yes
        ADDWF Checksum, F
        CALL TX_Serial
        MOVLW My_Key5
        BTFSC Try_Def, 0 ;failed previous scan?
        MOVLW Def_Key5 ;yes
        ADDWF Checksum, F
        CALL TX_Serial
        MOVLW My_Key6
        BTFSC Try_Def, 0 ;failed previous scan?
        MOVLW Def_Key6 ;yes
        ADDWF Checksum, F
        CALL TX_Serial ;end Key A
        MOVFW UID1 ;tag UID (4 bytes)
        ADDWF Checksum, F
        CALL TX_Serial
        MOVFW UID2
        ADDWF Checksum, F
        CALL TX_Serial
        MOVFW UID3
        ADDWF Checksum, F
        CALL TX_Serial
        MOVFW UID4
        ADDWF Checksum, F
        CALL TX_Serial ;end tag UID
        CALL Do_Chksm
        CALL Find_Resp
        BTFSS TFI_Found, 0
        GOTO Bad_Scan
        MOVFW Cmd_Stat
        BTFSS STATUS, Z
        GOTO Bad_Scan
        RETURN

;Read tag data from the defined data block of the authorized sector
Read_Tag CALL Preamble
        MOVLW 0x05
        CALL TX_Serial
        MOVLW 0xFB
        CALL TX_Serial
        MOVLW 0xD4
        MOVWF Checksum
        CALL TX_Serial
        MOVLW 0x40 ;InDataExchange
        ADDWF Checksum, F
        CALL TX_Serial
        MOVLW 0x01 ;number of targets
        ADDWF Checksum, F
        CALL TX_Serial
        MOVLW 0x30 ;read block (16 bytes)
        ADDWF Checksum, F
        CALL TX_Serial
        MOVFW Tag_Blk_Num ;block number (0-63)
        ADDWF Checksum, F
        CALL TX_Serial
        GOTO Do_Chksm

;Initiates a write to the tag. Other routines are then called to
;store/modify data or change the keys.
Write_Tag CALL Preamble
        MOVLW 0x15
        CALL TX_Serial
        MOVLW 0xEB
        CALL TX_Serial
        MOVLW 0xD4
        MOVWF Checksum
        CALL TX_Serial
        MOVLW 0x40 ;InDataExchange
        ADDWF Checksum, F
        CALL TX_Serial
        MOVLW 0x01 ;number of targets
        ADDWF Checksum, F
        CALL TX_Serial
        MOVLW 0xA0 ;write block (16 bytes)
        ADDWF Checksum, F
        CALL TX_Serial
        MOVFW Tag_Blk_Num ;block number (0-63)
        ADDWF Checksum, F
        CALL TX_Serial
        RETURN

;Sends credit data as part of the Write_Tag command.
;Formatted as 4 bytes credit, 4 bytes 1's complement of credit,
;8 bytes of zeros. Called once for the data block and once for
;the backup block.
Send_Data MOVFW Millions
        ADDWF Checksum, F
        CALL TX_Serial
        MOVFW Ten_Thou
        ADDWF Checksum, F
        CALL TX_Serial
        MOVFW Hundreds
        ADDWF Checksum, F
        CALL TX_Serial
        MOVFW Ones
        ADDWF Checksum, F
        CALL TX_Serial
        COMF Millions, W
        ADDWF Checksum, F
        CALL TX_Serial
        COMF Ten_Thou, W
        ADDWF Checksum, F
        CALL TX_Serial
        COMF Hundreds, W
        ADDWF Checksum, F
        CALL TX_Serial
        COMF Ones, W
        ADDWF Checksum, F
        CALL TX_Serial
        MOVLW 0x00
        CALL TX_Serial
        MOVLW 0x00
        CALL TX_Serial
        MOVLW 0x00
        CALL TX_Serial
        MOVLW 0x00
        CALL TX_Serial
        MOVLW 0x00
        CALL TX_Serial
        MOVLW 0x00
        CALL TX_Serial
        MOVLW 0x00
        CALL TX_Serial
        MOVLW 0x00
        CALL TX_Serial
        CALL Do_Chksm
        CALL Find_Resp
        BTFSS TFI_Found, 0
        GOTO Bad_Write
        MOVFW Cmd_Stat
        BTFSS STATUS, Z
        GOTO Bad_Write
        RETURN

;Sends key data as part of the Write_Tag command.
;Formated as 6 bytes Key A, 3 bytes write access flags,
;1 byte Don't Care, 6 bytes Key B.
Send_Keys MOVLW My_Key1 ;write Key A
        ADDWF Checksum, F
        CALL TX_Serial
        MOVLW My_Key2
        ADDWF Checksum, F
        CALL TX_Serial
        MOVLW My_Key3
        ADDWF Checksum, F
        CALL TX_Serial
        MOVLW My_Key4
        ADDWF Checksum, F
        CALL TX_Serial
        MOVLW My_Key5
        ADDWF Checksum, F
        CALL TX_Serial
        MOVLW My_Key6
        ADDWF Checksum, F
        CALL TX_Serial
        MOVLW 0xFF ;write access flags
        ADDWF Checksum, F
        CALL TX_Serial
        MOVLW 0x07
        ADDWF Checksum, F
        CALL TX_Serial
        MOVLW 0x80
        ADDWF Checksum, F
        CALL TX_Serial
        MOVLW 0x69 ;don't care byte
        ADDWF Checksum, F
        CALL TX_Serial
        MOVLW My_Key1 ;write Key B
        ADDWF Checksum, F
        CALL TX_Serial
        MOVLW My_Key2
        ADDWF Checksum, F
        CALL TX_Serial
        MOVLW My_Key3
        ADDWF Checksum, F
        CALL TX_Serial
        MOVLW My_Key4
        ADDWF Checksum, F
        CALL TX_Serial
        MOVLW My_Key5
        ADDWF Checksum, F
        CALL TX_Serial
        MOVLW My_Key6
        ADDWF Checksum, F
        CALL TX_Serial
        CALL Do_Chksm
        CALL Find_Resp
        BTFSS TFI_Found, 0
        GOTO Bad_Write
        MOVFW Cmd_Stat
        BTFSS STATUS, Z
        GOTO Bad_Write
        RETURN

;Called to initialize a new tag or one with corrupted data
Init_Tag CALL Auth_Tag
        MOVLW Trail_Blk
        MOVWF Tag_Blk_Num
        CALL Write_Tag
        CALL Send_Keys
        MOVLW Data_Blk ;Credits Block
        MOVWF Tag_Blk_Num
        CLRF Millions
        CLRF Ten_Thou
        CLRF Hundreds
        CLRF Ones
        CALL Write_Tag
        CALL Send_Data
        MOVLW Bkup_Blk ;Backup Block
        MOVWF Tag_Blk_Num
        CALL Write_Tag
        CALL Send_Data
        CLRF Try_Def
        CLRF Reinit_Tag
        GOTO Tag_Done

;Gets the credit value from the tag and verifies it against the
;complemented copy. Returns '1' if valid or '0' if invalid.
Get_Credit CALL Find_Resp
        BTFSS TFI_Found, 0
        GOTO Bad_Read ;no
        MOVFW Cmd_Stat
        BTFSS STATUS, Z ;valid status?
        GOTO Bad_Read ;no
        MOVLW LOW Byte1
        ADDWF Targ_Ptr, W ;index to data
        ADDLW d'3' ;offset from TFI to Data
        MOVWF FSR
        MOVFW INDF
        MOVWF Millions
        INCF FSR, F
        MOVFW INDF
        MOVWF Ten_Thou
        INCF FSR, F
        MOVFW INDF
        MOVWF Hundreds
        INCF FSR, F
        MOVFW INDF
        MOVWF Ones
        ;Read 1's complement version
        INCF FSR, F
        COMF INDF, W
        MOVWF Comp_4
        INCF FSR, F
        COMF INDF, W
        MOVWF Comp_3
        INCF FSR, F
        COMF INDF, W
        MOVWF Comp_2
        INCF FSR, F
        COMF INDF, W
        MOVWF Comp_1
        ;verify values
        MOVFW Millions
        SUBWF Comp_4, W
        BTFSS STATUS, Z ;match?
        RETLW d'0' ;no
        MOVFW Ten_Thou
        SUBWF Comp_3, W
        BTFSS STATUS, Z ;match?
        RETLW d'0' ;no
        MOVFW Hundreds
        SUBWF Comp_2, W
        BTFSS STATUS, Z ;match?
        RETLW d'0' ;no
        MOVFW Ones
        SUBWF Comp_1, W
        BTFSS STATUS, Z ;match?
        RETLW d'0' ;no
        RETLW d'1' ;valid data

Get_Backup MOVLW Bkup_Blk ;Backup Block
        MOVWF Tag_Blk_Num
        CALL Read_Tag
        CALL Get_Credit
        SUBLW d'1'
        BTFSS STATUS, Z ;valid data?
        GOTO Bad_Card ;no
        RETURN

Match_Fail CALL Bad_Data
        CALL Delay1sec
        CALL Delay1sec
        CALL Get_Backup
        MOVLW Data_Blk ;Data Block
        MOVWF Tag_Blk_Num
        CALL Write_Tag
        CALL Send_Data
        CALL Read_Tag
        CALL Get_Credit
        SUBLW d'1'
        BTFSS STATUS, Z ;valid data?
        GOTO Bad_Card ;no
        CALL Data_Fixed
        CALL Delay1sec
        CALL Delay1sec
        CALL Disp_Credit
        CALL Delay1sec
        CALL Delay1sec
        CALL Done_Msg
        GOTO Scan_Loop

Inc_Credit MOVLW Inc1
        ADDWF Ones, F
        DAA Ones
        BTFSC Carry, 0
        INCF Hundreds, F
        MOVLW Inc100
        ADDWF Hundreds, F
        DAA Hundreds
        BTFSC Carry, 0
        INCF Ten_Thou, F
        MOVLW Inc10_000
        ADDWF Ten_Thou, F
        DAA Ten_Thou
        BTFSC Carry, 0
        INCF Millions, F
        MOVLW Inc_Mill
        ADDWF Millions, F
        DAA Millions
        BTFSC Carry, 0
        GOTO Full_Credit
        MOVLW Bkup_Blk ;Backup Block
        MOVWF Tag_Blk_Num
        CALL Write_Tag
        CALL Send_Data
        MOVLW Data_Blk ;Data Block
        MOVWF Tag_Blk_Num
        CALL Write_Tag
        CALL Send_Data
        CALL Read_Tag
        CALL Get_Credit
        SUBLW d'1'
        BTFSS STATUS, Z ;valid data?
        GOTO Match_Fail ;no
        CALL Disp_Credit
        RETURN

Dec_Credit MOVLW Dec1
        SUBWF Ones, F
        DAS Ones
        BTFSC Borrow, 0
        DECF Hundreds, F
        MOVLW Dec100
        SUBWF Hundreds, F
        DAS Hundreds
        BTFSC Borrow, 0
        DECF Ten_Thou, F
        MOVLW Dec10_000
        SUBWF Ten_Thou, F
        DAS Ten_Thou
        BTFSC Borrow, 0
        DECF Millions, F
        MOVLW Dec_Mill
        SUBWF Millions, F
        DAS Millions
        BTFSC Borrow, 0
        GOTO Bad_Credit
        MOVLW Bkup_Blk ;Backup Block
        MOVWF Tag_Blk_Num
        CALL Write_Tag
        CALL Send_Data
        MOVLW Data_Blk ;Data Block
        MOVWF Tag_Blk_Num
        CALL Write_Tag
        CALL Send_Data
        CALL Read_Tag
        CALL Get_Credit
        SUBLW d'1'
        BTFSS STATUS, Z ;valid data?
        GOTO Match_Fail ;no
        CALL Disp_Credit
        RETURN

Preamble CLRF New_Msg
        CLRF Byte_Count
        MOVLW LOW Byte1 ;clear receive buffer
preamble1 MOVWF FSR
        MOVLW 0x00
        MOVWF INDF
        INCF FSR, F
        INCF Byte_Count, F
        MOVLW d'31'
        SUBWF Byte_Count, W
        BTFSS STATUS, Z
        GOTO preamble1
        MOVLW 0x00
        CALL TX_Serial
        MOVLW 0x00
        CALL TX_Serial
        MOVLW 0xFF
        CALL TX_Serial
        RETURN

Do_Chksm COMF Checksum, F ;negate value (1's complement)
        INCF Checksum, W ;add 1 for 2's complement
        CALL TX_Serial
Postamble MOVLW 0x00
        CALL TX_Serial
        CALL Delay100ms
        RETURN

Find_Resp CLRF TFI_Found
        MOVFW Byte_Count
        SUBLW d'15'
        BTFSS STATUS, C ;more than just ACK?
        GOTO find_resp1 ;yes
        CLRF New_Msg
        RETURN
find_resp1 CALL Send_ACK
        MOVLW d'20'
        MOVWF Read_Cnt
        MOVLW Resp_TFI
        MOVLW Resp_TFI ;Response TFI
        CALL Read_Buff
        INCF Targ_Ptr, W
        BTFSS STATUS, Z ;target found?
        BSF TFI_Found, 0
        RETURN

;-----------------------------------
; Data conversion routines
;-----------------------------------

;Find the first non-zero frequency digit for display
Find_First MOVF Millions, F
        BTFSC STATUS, Z
        GOTO Find1
        SWAPF Millions, W
        ANDLW 0x0F
        BTFSS STATUS, Z
        GOTO Disp_10M
        GOTO Disp_1M
Find1 MOVF Ten_Thou, F
        BTFSC STATUS, Z
        GOTO Find2
        SWAPF Ten_Thou, W
        ANDLW 0x0F
        BTFSS STATUS, Z
        GOTO Disp_100k
        GOTO Disp_10k
Find2 MOVF Hundreds, F
        BTFSC STATUS, Z
        GOTO Find3
        SWAPF Hundreds, W
        ANDLW 0x0F
        BTFSS STATUS, Z
        GOTO Disp_1k
        GOTO Disp_100
Find3 SWAPF Ones, W
        ANDLW 0x0F
        BTFSS STATUS, Z
        GOTO Disp_10
        GOTO Disp_1

;Convert frequency values to ASCII for display
Disp_10M SWAPF Millions, W
        ANDLW 0x0F
        IORLW 0x30
        CALL Write_LCD
Disp_1M MOVF Millions, W
        ANDLW 0x0F
        IORLW 0x30
        CALL Write_LCD
        MOVLW ','
        CALL Write_LCD
Disp_100k SWAPF Ten_Thou, W
        ANDLW 0x0F
        IORLW 0x30
        CALL Write_LCD
Disp_10k MOVF Ten_Thou, W
        ANDLW 0x0F
        IORLW 0x30
        CALL Write_LCD
Disp_1k SWAPF Hundreds, W
        ANDLW 0x0F
        IORLW 0x30
        CALL Write_LCD
        MOVLW ','
        CALL Write_LCD
Disp_100 MOVF Hundreds, W
        ANDLW 0x0F
        IORLW 0x30
        CALL Write_LCD
Disp_10 SWAPF Ones, W
        ANDLW 0x0F
        IORLW 0x30
        CALL Write_LCD
Disp_1 MOVF Ones, W
        ANDLW 0x0F
        IORLW 0x30
        CALL Write_LCD
        RETURN

;-----------------------------------
; Receive Buffer Utilities
;-----------------------------------

Read_Buff CLRF Targ_Ptr
read_buff1 MOVLW LOW Byte1
        ADDWF Targ_Ptr, W
        MOVWF FSR
        MOVFW INDF ;read from memory as indexed by Targ_Ptr
        SUBLW Resp_TFI ;Response TFI
        BTFSS STATUS, Z ;found target value?
        GOTO read_buff2 ;no
        INCF FSR, F
        MOVFW INDF ;command echo (=command+1)
        MOVWF Cmd_Echo
        INCF FSR, F
        MOVFW INDF ;command status
        MOVWF Cmd_Stat
        RETURN
read_buff2 INCF Targ_Ptr, F
        DECF Read_Cnt, F
        BTFSS STATUS, Z ;completed read?
        GOTO read_buff1 ;no
        MOVLW 0xFF
        MOVWF Targ_Ptr
        RETURN ;value not found

;Display receive buffer
Disp_Buff CLRF New_Msg
        CLRF Dummy
        MOVLW Max_Line
        MOVWF Line_Brk
        CALL Clear_LCD
        BTFSC Disp_All, 0 ;display entire buffer?
        GOTO disp_loop ;yes
        CALL Find_Resp ;no, just display data
        MOVFW Targ_Ptr
        BTFSC STATUS, Z ;found valid response?
        RETURN ;no
        ADDLW d'3' ;point to start of data
        MOVWF Dummy
        ADDWF Line_Brk, F
        MOVLW d'16'
        MOVWF Byte_Count
disp_loop MOVLW LOW Byte1
        ADDWF Dummy, W
        MOVWF FSR
        MOVFW INDF ;read from memory as indexed by Dummy
        CALL Make_ASCII
        INCF Dummy, F
        DECF Byte_Count, F
        BTFSC STATUS, Z
        RETURN
        MOVFW Line_Brk
        SUBWF Dummy, W
        BTFSS STATUS, Z ;LCD Line1 full?
        GOTO disp_loop ;no
        CALL Init_Line2
        GOTO disp_loop

;Convert HEX to ASCII for LCD
Make_ASCII MOVWF BCD_Byte
        SWAPF BCD_Byte, W
        ANDLW 0x0F
        IORLW 0x30
        MOVWF Temp_ASC
        SUBLW 0x39 ;check to see if A-F
        BTFSC STATUS, C
        GOTO Mk_ASCII_1
        MOVLW d'7'
        ADDWF Temp_ASC, F
Mk_ASCII_1 MOVFW Temp_ASC
        CALL Write_LCD
        MOVFW BCD_Byte
        ANDLW 0x0F
        IORLW 0x30
        MOVWF Temp_ASC
        SUBLW 0x39 ;check to see if A-F
        BTFSC STATUS, C
        GOTO Mk_ASCII_2
        MOVLW d'7'
        ADDWF Temp_ASC, F
Mk_ASCII_2 MOVFW Temp_ASC
        CALL Write_LCD
        RETURN

;-----------------------------------
; Serial Port Routines
;-----------------------------------

Init_Serial CLRF New_Msg
        CLRF Byte_Count
        BSF TXSTA, BRGH ;high speed mode
        BSF BAUDCTL, BRG16
        MOVLW d'16'
        MOVWF SPBRG ;115k baud at 8-MHz clock
        MOVFW RCREG ;clear interrupt
        BSF TXSTA, TXEN ;enable transmitter
        BSF RCSTA, SPEN ;serial port enable
        BSF RCSTA, CREN ;continuous RX enable
        BSF INTCON, PEIE ;peripheral interrupt enable
        BSF INTCON, GIE ;general interrupt enable
        RETURN

TX_Serial BTFSS PIR1, TXIF ;TX interrupt: 1 = TXREG is empty
        GOTO TX_Serial ;not empty
        MOVWF TXREG ;ok to transmit
        RETURN

Overflow BCF RCSTA, SPEN ;disable serial port
        MOVFW RCREG ;clear interrupt
        BSF RCSTA, SPEN ;enable serial port (reset)
        RETURN

;----------------------------------------
; LCD Routines
;----------------------------------------

Init_LCD CALL Delay100ms ;allow LCD time to reset
        MOVLW Cmnd_Mode ;all init done in LCD command mode
        MOVWF Reg_Select
        MOVLW 0x03 ;LCD sees 30 hex
        CALL Cmd_8_Bit
        CALL Delay4ms ;Delay greater than 4.1ms
        CALL Delay100us
        MOVLW 0x03 ;LCD sees 30 hex
        CALL Cmd_8_Bit
        CALL Delay100us ;Delay greater than 100us
        MOVLW 0x03 ;LCD sees 30 hex
        CALL Cmd_8_Bit
        CALL Delay100us ;Delay greater than 100us
        MOVLW 0x02 ;Set 4-bit mode (LCD sees 20 hex)
        CALL Cmd_8_Bit
        CALL Delay100us ;Delay greater than 100us
        MOVLW 0x28 ;Set for 4-bit mode, 16 chars, 2 lines
        CALL Write_LCD
        CALL Delay100us ;Delay greater than 100us
        MOVLW 0x01 ;clear display
        CALL Write_LCD
        CALL Delay4ms ;Delay greater than 4ms
        MOVLW 0x06 ;Entry mode, increment DDRAM, no shift
        CALL Write_LCD
        CALL Delay100us ;Delay greater than 100us
        MOVLW 0x0C ;Display on, cursor off
        CALL Write_LCD
        CALL Delay100us ;Delay greater than 100us
        MOVLW Data_Mode
        MOVWF Reg_Select
        RETURN

Cmd_8_Bit MOVWF LCD_PORT ;byte to write will be in W
        BCF Select ;set for command mode
        BSF Enable ;write data to LCD
        NOP
        BCF Enable
        RETURN

Write_LCD MOVWF LCD_Data ;byte to write will be in W
        SWAPF LCD_Data, W ;send upper nibble
        ANDLW 0x0F ;clear upper 4 bits of W
        MOVWF LCD_PORT
        BSF Select ;preset for data mode
        BTFSS Reg_Select, 0 ;0 = command mode, 1 = data mode
        BCF Select ;set for command mode instead
        CALL Delay50us
        BSF Enable ;write data to LCD
        NOP
        BCF Enable
        MOVFW LCD_Data ;send lower nibble
        ANDLW 0x0F ;clear upper 4 bits of W
        MOVWF LCD_PORT
        BSF Select ;preset for data mode
        BTFSS Reg_Select, 0 ;0 = command mode, 1 = data mode
        BCF Select ;set for command mode instead
        BSF Enable ;write data to LCD
        NOP
        BCF Enable
        RETURN

Init_Line2 MOVLW Cmnd_Mode
        MOVWF Reg_Select
        MOVLW 0xC0 ;write at start of line 2 (address 0x40)
        CALL Write_LCD
        CALL Delay100us
        MOVLW Data_Mode
        MOVWF Reg_Select
        RETURN

Clear_LCD MOVLW Cmnd_Mode
        MOVWF Reg_Select
        MOVLW 0x01 ;clear display
        CALL Write_LCD
        CALL Delay1ms
        CALL Delay1ms
        CALL Delay1ms
        CALL Delay1ms
        MOVLW Data_Mode
        MOVWF Reg_Select
        RETURN

Scan_Msg CALL Clear_LCD
        MOVLW ' '
        CALL Write_LCD
        MOVLW 'R'
        CALL Write_LCD
        MOVLW 'E'
        CALL Write_LCD
        MOVLW 'A'
        CALL Write_LCD
        MOVLW 'D'
        CALL Write_LCD
        MOVLW 'Y'
        CALL Write_LCD
        MOVLW ' '
        CALL Write_LCD
        MOVLW 'T'
        CALL Write_LCD
        MOVLW 'O'
        CALL Write_LCD
        MOVLW ' '
        CALL Write_LCD
        MOVLW 'S'
        CALL Write_LCD
        MOVLW 'C'
        CALL Write_LCD
        MOVLW 'A'
        CALL Write_LCD
        MOVLW 'N'
        CALL Write_LCD
        CALL Delay1sec
        RETURN

Bad_Scan CALL Clear_LCD
        MOVLW 'B'
        CALL Write_LCD
        MOVLW 'A'
        CALL Write_LCD
        MOVLW 'D'
        CALL Write_LCD
        MOVLW ' '
        CALL Write_LCD
        MOVLW 'S'
        CALL Write_LCD
        MOVLW 'C'
        CALL Write_LCD
        MOVLW 'A'
        CALL Write_LCD
        MOVLW 'N'
        CALL Write_LCD
        COMF Try_Def, F ;toggle flag
Tilt BSF WDTCON, SWDTEN ;force watchdog timeout
tilt1 GOTO tilt1

Bad_Write CALL Clear_LCD
        MOVLW 'B'
        CALL Write_LCD
        MOVLW 'A'
        CALL Write_LCD
        MOVLW 'D'
        CALL Write_LCD
        MOVLW ' '
        CALL Write_LCD
        MOVLW 'W'
        CALL Write_LCD
        MOVLW 'R'
        CALL Write_LCD
        MOVLW 'I'
        CALL Write_LCD
        MOVLW 'T'
        CALL Write_LCD
        MOVLW 'E'
        CALL Write_LCD
        GOTO Tilt

Bad_Read CALL Clear_LCD
        MOVLW 'B'
        CALL Write_LCD
        MOVLW 'A'
        CALL Write_LCD
        MOVLW 'D'
        CALL Write_LCD
        MOVLW ' '
        CALL Write_LCD
        MOVLW 'R'
        CALL Write_LCD
        MOVLW 'E'
        CALL Write_LCD
        MOVLW 'A'
        CALL Write_LCD
        MOVLW 'D'
        CALL Write_LCD
        GOTO Tilt

Bad_Card CALL Clear_LCD
        MOVLW 'B'
        CALL Write_LCD
        MOVLW 'A'
        CALL Write_LCD
        MOVLW 'D'
        CALL Write_LCD
        MOVLW ' '
        CALL Write_LCD
        MOVLW 'C'
        CALL Write_LCD
        MOVLW 'A'
        CALL Write_LCD
        MOVLW 'R'
        CALL Write_LCD
        MOVLW 'D'
        CALL Write_LCD
        BSF Reinit_Tag, 0
        GOTO Tilt

Bad_Data CALL Clear_LCD
        MOVLW 'D'
        CALL Write_LCD
        MOVLW 'A'
        CALL Write_LCD
        MOVLW 'T'
        CALL Write_LCD
        MOVLW 'A'
        CALL Write_LCD
        MOVLW ' '
        CALL Write_LCD
        MOVLW 'C'
        CALL Write_LCD
        MOVLW 'O'
        CALL Write_LCD
        MOVLW 'R'
        CALL Write_LCD
        MOVLW 'R'
        CALL Write_LCD
        MOVLW 'U'
        CALL Write_LCD
        MOVLW 'P'
        CALL Write_LCD
        MOVLW 'T'
        CALL Write_LCD
        MOVLW ':'
        CALL Write_LCD
        CALL Init_Line2
        MOVLW 'C'
        CALL Write_LCD
        MOVLW 'H'
        CALL Write_LCD
        MOVLW 'E'
        CALL Write_LCD
        MOVLW 'C'
        CALL Write_LCD
        MOVLW 'K'
        CALL Write_LCD
        MOVLW 'I'
        CALL Write_LCD
        MOVLW 'N'
        CALL Write_LCD
        MOVLW 'G'
        CALL Write_LCD
        MOVLW ' '
        CALL Write_LCD
        MOVLW 'B'
        CALL Write_LCD
        MOVLW 'A'
        CALL Write_LCD
        MOVLW 'C'
        CALL Write_LCD
        MOVLW 'K'
        CALL Write_LCD
        MOVLW 'U'
        CALL Write_LCD
        MOVLW 'P'
        CALL Write_LCD
        CALL Delay1sec
        RETURN

Data_Fixed CALL Clear_LCD
        MOVLW 'D'
        CALL Write_LCD
        MOVLW 'A'
        CALL Write_LCD
        MOVLW 'T'
        CALL Write_LCD
        MOVLW 'A'
        CALL Write_LCD
        MOVLW ' '
        CALL Write_LCD
        MOVLW 'R'
        CALL Write_LCD
        MOVLW 'E'
        CALL Write_LCD
        MOVLW 'P'
        CALL Write_LCD
        MOVLW 'A'
        CALL Write_LCD
        MOVLW 'I'
        CALL Write_LCD
        MOVLW 'R'
        CALL Write_LCD
        MOVLW 'E'
        CALL Write_LCD
        MOVLW 'D'
        CALL Write_LCD
        CALL Delay1sec
        RETURN

Auth_Msg CALL Clear_LCD
        MOVLW 'A'
        CALL Write_LCD
        MOVLW 'U'
        CALL Write_LCD
        MOVLW 'T'
        CALL Write_LCD
        MOVLW 'H'
        CALL Write_LCD
        MOVLW 'E'
        CALL Write_LCD
        MOVLW 'N'
        CALL Write_LCD
        MOVLW 'T'
        CALL Write_LCD
        MOVLW 'I'
        CALL Write_LCD
        MOVLW 'C'
        CALL Write_LCD
        MOVLW 'A'
        CALL Write_LCD
        MOVLW 'T'
        CALL Write_LCD
        MOVLW 'E'
        CALL Write_LCD
        MOVLW 'D'
        CALL Write_LCD
        CALL Delay1sec
        RETURN

Done_Msg CALL Clear_LCD
        MOVLW 'R'
        CALL Write_LCD
        MOVLW 'E'
        CALL Write_LCD
        MOVLW 'M'
        CALL Write_LCD
        MOVLW 'O'
        CALL Write_LCD
        MOVLW 'V'
        CALL Write_LCD
        MOVLW 'E'
        CALL Write_LCD
        MOVLW ' '
        CALL Write_LCD
        MOVLW 'T'
        CALL Write_LCD
        MOVLW 'A'
        CALL Write_LCD
        MOVLW 'G'
        CALL Write_LCD
        CALL Delay1sec
        CALL Delay1sec
        RETURN

Disp_UID CALL Clear_LCD
        MOVLW 'U'
        CALL Write_LCD
        MOVLW 'I'
        CALL Write_LCD
        MOVLW 'D'
        CALL Write_LCD
        MOVLW ':'
        CALL Write_LCD
        MOVLW ' '
        CALL Write_LCD
        MOVFW UID1
        CALL Make_ASCII
        MOVFW UID2
        CALL Make_ASCII
        MOVFW UID3
        CALL Make_ASCII
        MOVFW UID4
        CALL Make_ASCII
        CALL Delay1sec
        CALL Delay1sec
        RETURN

Disp_Credit CALL Clear_LCD
        MOVLW 'C'
        CALL Write_LCD
        MOVLW 'R'
        CALL Write_LCD
        MOVLW 'E'
        CALL Write_LCD
        MOVLW 'D'
        CALL Write_LCD
        MOVLW 'I'
        CALL Write_LCD
        MOVLW 'T'
        CALL Write_LCD
        MOVLW 'S'
        CALL Write_LCD
        MOVLW ':'
        CALL Write_LCD
        CALL Init_Line2
        CALL Find_First
        CALL Delay1sec
        RETURN

Bad_Credit CALL Clear_LCD
        MOVLW 'N'
        CALL Write_LCD
        MOVLW 'O'
        CALL Write_LCD
        MOVLW 'T'
        CALL Write_LCD
        MOVLW ' '
        CALL Write_LCD
        MOVLW 'E'
        CALL Write_LCD
        MOVLW 'N'
        CALL Write_LCD
        MOVLW 'O'
        CALL Write_LCD
        MOVLW 'U'
        CALL Write_LCD
        MOVLW 'G'
        CALL Write_LCD
        MOVLW 'H'
        CALL Write_LCD
        CALL Init_Line2
        MOVLW 'C'
        CALL Write_LCD
        MOVLW 'R'
        CALL Write_LCD
        MOVLW 'E'
        CALL Write_LCD
        MOVLW 'D'
        CALL Write_LCD
        MOVLW 'I'
        CALL Write_LCD
        MOVLW 'T'
        CALL Write_LCD
        MOVLW 'S'
        CALL Write_LCD
        GOTO Tilt

Full_Credit CALL Clear_LCD
        MOVLW 'W'
        CALL Write_LCD
        MOVLW 'A'
        CALL Write_LCD
        MOVLW 'L'
        CALL Write_LCD
        MOVLW 'L'
        CALL Write_LCD
        MOVLW 'E'
        CALL Write_LCD
        MOVLW 'T'
        CALL Write_LCD
        MOVLW ' '
        CALL Write_LCD
        MOVLW 'F'
        CALL Write_LCD
        MOVLW 'U'
        CALL Write_LCD
        MOVLW 'L'
        CALL Write_LCD
        MOVLW 'L'
        CALL Write_LCD
        GOTO Tilt

Tag_Done CALL Clear_LCD
        MOVLW 'T'
        CALL Write_LCD
        MOVLW 'A'
        CALL Write_LCD
        MOVLW 'G'
        CALL Write_LCD
        MOVLW ' '
        CALL Write_LCD
        MOVLW 'I'
        CALL Write_LCD
        MOVLW 'N'
        CALL Write_LCD
        MOVLW 'T'
        CALL Write_LCD
        MOVLW 'I'
        CALL Write_LCD
        MOVLW 'A'
        CALL Write_LCD
        MOVLW 'L'
        CALL Write_LCD
        MOVLW 'I'
        CALL Write_LCD
        MOVLW 'Z'
        CALL Write_LCD
        MOVLW 'E'
        CALL Write_LCD
        MOVLW 'D'
        CALL Write_LCD
        GOTO Tilt

;-----------------------------------
; Delay routines (8-MHz clock)
;-----------------------------------

Delay50us MOVLW d'24'
        GOTO Cntdwn

Delay100us MOVLW d'48'
        GOTO Cntdwn

Delay1ms MOVLW d'249'
        CALL Cntdwn
        MOVLW d'249'
        GOTO Cntdwn

Delay4ms CALL Delay1ms
        CALL Delay1ms
        CALL Delay1ms
        GOTO Delay1ms

Delay100ms MOVLW d'100'
        MOVWF Delay_Cnt
loop100ms CALL Delay1ms
        DECFSZ Delay_Cnt, F
        GOTO loop100ms
        RETURN

Delay250ms MOVLW d'250'
        MOVWF Delay_Cnt
loop250ms CALL Delay1ms
        DECFSZ Delay_Cnt, F
        GOTO loop250ms
        RETURN

Delay1sec CALL Delay250ms
        CALL Delay250ms
        CALL Delay250ms
        CALL Delay250ms
        RETURN

Cntdwn ADDLW -1 ;decrement W
        BTFSS STATUS, Z ;Zero flag set?
        GOTO Cntdwn ;No, keep looping
        RETURN ;Yes, timeout done
;-------------------------------------------------------------------------------

        END